## Slide 1: CSCI4430 Computer Networks Lecture 5: Application Layer – Video; cloud & datacenters
Hong Xu, Henry
CSE@CUHK, 2022
Material with thanks to Patrick Lee, Mosharaf Chowdhury, Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Agenda
Video streaming
Datacenter applications

## Slide 3: How is video different?
Often too large to send in one GET
Doesn’t even make sense even if it’s possible
  Users may skip forward! ⇒ save bandwidth wastage
  User connection quality may change (e.g., switching from WiFi to LTE) ⇒ lower resolution to save bandwidth
Our focus is on stored video (i.e., not live)

## Slide 4: Why video is important?
Dominates the global Internet traffic landscape
  About 60%, i.e., every 3 of 5 bytes in 2020!
Major sources
  Netflix
  YouTube
  …

## Slide 5: The video medium
Video is a sequence of images/frames displayed at a constant rate (moving pictures)
Digital image is an array of pixels, each pixel represented by bits
Examples:
  Single frame image encoding: 1024x1024 pixels, 24 bits/pixel ⇒ 3 MB/image
  Movies: 24 frames/sec ⇒ 72 MB/sec
  TV: 30 frames/sec ⇒ 90 MB/sec

## Slide 6: The video medium (cont’d)
Compression is key
  Lots of algorithms to compress
The same video can be (and typically is) compressed to multiple quality levels
  E.g., 480p, 720p, 1080p, 4K
Why multiple resolutions?
  Adapt to conditions
……………………..
……………….…….
spatial coding example: instead of sending N values of same color (all purple), send only two values: color value (purple) and number of repeated values (N)
frame i
frame i+1
temporal coding example: instead of sending complete frame at i+1, send only differences from frame i

## Slide 7: How do we serve video?
It’s in the name!
  Video streaming

## Slide 8: HTTP streaming
Video is stored at an HTTP server with a URL
Clients send a GET request for the URL
Server sends the video file as a stream
Client first buffers for a while. Why?
  To minimize interruptions later
Once the buffer reaches a threshold
  The video plays in the foreground
  More frames are downloaded in the background

## Slide 9: HTTP streaming
video
recorded (e.g., 30 frames/sec)
2. video
sent
Cumulative data
streaming: at this time, client
playing out early part of video,
while server still sending later
part of video
network delay
(fixed in this example)
time
3. video received,
played out at client
(30 frames/sec)

## Slide 10: Challenges
Absorb network delay variations
Handle user interactions
  Jump forward, fast-forward, rewind, pause
Handle packet loss, retransmission etc.

## Slide 11: HTTP streaming: Revisited
constant bit
rate video
transmission
Cumulative data
time
variable
network
delay
client video
reception
constant bit
rate video
playout at client
client playout
delay
buffered
video
Client-side buffering and playout delay: compensate for network-added delay, delay jitter

## Slide 12: Issues with HTTP streaming
Same bitrate for all clients
  Clients can have very different network conditions
  Clients network conditions can change over time
Cannot dynamically adapt to conditions

## Slide 13: DASH : Dynamic Adaptive Streaming over HTTP
Keep multiple resolutions of the same video
  Stored in a manifest file in the HTTP server
Client asks for the manifest file first to learn about the options
Asks for chunks at a time and measures available bandwidth while they are downloaded
  Low bandwidth ⇒ switch to lower bitrate
  High bandwidth ⇒ switch to higher bitrate

## Slide 14: DASH
server:
  divides video file into many chunks
  each chunk encoded at multiple different rates
  different rate encodings stored in different files
  files replicated in various CDN nodes
  manifest file: provides URLs for different chunks
client:
  periodically estimates server-to-client bandwidth
  consulting manifest, requests one chunk at a time
    chooses maximum coding rate sustainable given current bandwidth
    can choose different coding rates at different points in time (depending on available bandwidth at time), and from different servers
client
?
...
...

## Slide 15: DASH
“intelligence” at client: client determines
  when to request a chunk (so that buffer starvation, or overflow does not occur)
  what bit rate to request (higher quality when more bandwidth available) -> adaptive bit-rate (ABR)
  where to request chunk (can request from URL server that is “close” to client or has high available bandwidth)
Streaming video = encoding + DASH + playout buffering
...
...
client
?

## Slide 16: Video streaming with CDN
Video distribution relies heavily on CDN

## Slide 17: Short videos
Differences?
  Short duration, typically <30s
  No fast-forward; swipe to next
Serving technologies
  No ABR
  Prefetching: download chunks of next video in advance
Interesting research area

## Slide 18: Cloud, datacenters

## Slide 19: Who’s serving Web services?
User
Server
HTTP GET

## Slide 20: Who’s serving Web services?
User
Server
HTTP Response
<html>
<body>
... …
</body>
</html>

## Slide 21: Cloud datacenters run the world
Source: Google
https://www.google.com/about/datacenters/

## Slide 22: Cloud datacenters run the world
Source: Google

## Slide 23: Cloud datacenters run the world
Source: Google

## Slide 24: How big is a datacenter (DC)?
1M servers/site [Microsoft/Amazon/Google]
> $1B to build one site [Facebook]
>$20M/month/site operational costs [MS’09]
Data center hardware spending grew to $177 billion in 2017. [Gartner report]
But only O(10-100) sites

## Slide 25: Implications (1)
Scale
  Need scalable designs
  Low-cost designs: e.g., use commodity technology
  High utilization (efficiency): e.g., >60% avg. utilization
    Contrast: avg. utilization on Internet links often ~30%
  Tolerate frequent failure
    Large number of (low cost) components
  Automate

## Slide 26: Implications (2)
Service model: clouds / multi-tenancy
  Performance guarantees
  Isolation guarantees
  Portability

## Slide 27: Applications
Common theme: parallelism
  Applications decomposed into tasks
  Running in parallel on different machines
Two common paradigms
  Partition-Aggregate
  Map-Reduce

## Slide 28: Partition-Aggregate
eecs 489
Top-level Aggregator
Mid-level Aggregators
Workers

## Slide 29: Partition-Aggregate
eecs 489
Top-level Aggregator
Mid-level Aggregators
Workers

## Slide 30: End-to-end response time
Less than 200 milliseconds between receiving user query in the browser and displaying the results
  RTT = O(10) to 100 milliseconds
  What remains?
Next time, when the page is not loading fast enough, think about the poor servers working for you 

## Slide 31: Applications
Common theme: parallelism
  Applications decomposed into tasks
  Running in parallel on different machines
Two common paradigms
  Partition-Aggregate
  Map-Reduce

## Slide 32: Map-Reduce
Reduce Stage
Map Stage
The most popular software that follows this paradigm is Apache Spark

## Slide 33: Datacenter networks
Server
ToR Switch
Aggregation

## Slide 34: Datacenter networks (Cont.)
Rack
Aggregation
Core

## Slide 35: Datacenter traffic
Rack
Aggregation
Core
North-South Traffic
East-West Traffic

## Slide 36: East-West traffic
Traffic between servers in the datacenter
Communication within “big data” computations
Traffic may shift on small timescales (< minutes)

## Slide 37: Datacenter traffic characteristics
Two key characteristics
  Most flows are small
  Most bytes come from large flows
Applications want
  High bandwidth (large flows)
  Low latency (small flows)

## Slide 38: Datacenter traffic characteristics
A. Roy et al. Inside the social network’s (datacenter) network. In Proc. of ACM SIGCOMM, 2015.

## Slide 39: High bandwidth
Ideal: Each server can talk to any other server at its full access link rate
Conceptually: Datacenter network as one giant switch

## Slide 40: Datacenter network as one giant switch

## Slide 41: Datacenter network as one giant switch

## Slide 42: Datacenter network as one giant switch
One
GIANT
Switch

## Slide 43: High bandwidth
Ideal: Each server can talk to any other server at its full access link rate
Conceptually: Datacenter network as one giant switch
  Would require a 10 Pbits/sec switch!
    1M ports (one port/server)
    10Gbps per port
Practical approach: build a network of switches (“fabric”) with high “bisection bandwidth”
  Each switch has practical #ports and link speeds

## Slide 44: Bisection bandwidth
Partition a network into two equal parts
Minimum bandwidth between the partitions is the bisection bandwidth
Full bisection bandwidth: bisection bandwidth in an N-node network is N/2 times the bandwidth of a single link
  Nodes of any two halves can communicate at full speed with each other

## Slide 45: Achieving full bisection bandwidth
Scale up
  Make links fatter toward the core of the network
Problem: Scaling up a traditional tree topology is expensive!
  Requires non-commodity / impractical / link and switch components
Solutions?
  Over-subscribe (i.e., provision less than full BBW)
  Better topologies

## Slide 46: Oversubscription
Need techniques to avoid congesting oversubscribed links!
10G
20G
40G
10G
10G
20G

## Slide 47: Oversubscription
Not enough bandwidth
  Oversubscription: Less bandwidth in the ToR-Agg links than all the server bandwidth in the rack
  Oversubscription ratio: Ratio between bandwidth underneath and bandwidth above
Not enough paths between server pairs
  Load balancing issues
  Failure recovery issues

## Slide 48: Better topologies
Rack
Aggregation
Core

## Slide 49: Better topologies
Rack
Aggregation
Core

## Slide 50: Clos topology
Multi-stage network
k pods, where each pod has two layers of k/2 switches
  k/2 ports up and k/2 down
All links have the same b/w
At most k3/4 machines
Example
  k = 4
  16 machines
For k=48, 27648 machines
Pod 1
Pod 2
Pod 3
Pod 4

## Slide 51: Challenges of scale-out design
Topology offers high bisection bandwidth
All other system components must be able to exploit this available capacity
  Routing must use all paths
  Transport protocol must fill all pipes (fast)

## Slide 52: Summary
Video streaming
  Too large to send, so stream it
  Dynamically adapt to the network and users
Cloud systems
  Forms the backend of modern web services
  Runs in datacenters where all the processing happens