## Slide 1: CSCI4430 Computer Networks Lecture10: Network Layer – Basics
Hong Xu, Henry
CSE@CUHK, 2022
Material with thanks to Patrick Lee, Mosharaf Chowdhury, Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Agenda
Network layer basics
The Internet Protocol (IP)

## Slide 3: Network layer
Present everywhere
Performs addressing, forwarding, and routing, among other tasks
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch

## Slide 4: Context and terminology
“End hosts”
“Clients”, “Users”
“End points”
“Interior Routers”
“Autonomous System (AS)” or “Domain” Region of a network under a single administrative entity
“Route” or “Path”
“Border Routers”

## Slide 5: Forwarding
111010010
MIT
umich.edu
mit.edu

## Slide 6: Forwarding
umich.edu
mit.edu
111010010
MIT
#1
#2
#3
#4
Destination | Next Hop
UMICH | 1
UCB | 3
MIT | 2
NYU | 4
Forwarding Table

## Slide 7: Forwarding
Directing a packet to the correct interface so that it progresses to its destination
  Local
How?
  Read address from packet header
  Search forwarding table

## Slide 8: Routing
Setting up network-wide forwarding tables to enable end-to-end communication
  Global
How?
  Using different routing protocols

## Slide 9: Forwarding vs. routing
Forwarding: “data plane”
  Directing one data packet
  Each router using local routing state
Routing: “control plane”
  Computing the forwarding tables that guide packets
  Jointly computed by routers using a distributed algorithm
Very different timescales!

## Slide 10: The IP layer

## Slide 11: Lecture 2: Layer encapsulation
HTTP
TCP
IP
HTTP
TCP
IP
IP
IP
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet

## Slide 12: Recall: IP packet
IP packet contains a header and payload
  Payload is opaque to the network
  Header is what we care about
  First end-to-end layer (going bottom-up)
IP header
IP payload
IP packet

## Slide 13: Designing the IP header
Think of the IP header as an interface
  Between the source and destination end-systems
  Between the source and network (routers)
Designing an interface
  What task(s) are we trying to accomplish?
  What information is needed to do it?
Header reflects information needed for basic tasks

## Slide 14: What are these tasks? (in network)
Parse packet
Carry packet to the destination
Deal with problems along the way
  Loops
  Corruption
  Packet too large
Accommodate evolution
Specify any special handling

## Slide 15: What information do we need?
Parse packet
Carry packet to the destination
Deal with problems along the way
  Loops
  Corruption
  Packet too large
Accommodate evolution
Specify any special handling

## Slide 16: What information do we need?
Parse packet
  IP version number (4 bits), packet length (16 bits)
Carry packet to the destination
  Destination’s IP address (32 bits)
Deal with problems along the way
  Loops:
  Corruption:
  Packet too large:

## Slide 17: What information do we need?
Parse packet
  IP version number (4 bits), packet length (16 bits)
Carry packet to the destination
  Destination’s IP address (32 bits)
Deal with problems along the way
  Loops: TTL (8 bits)
  Corruption: checksum (16 bits)
  Packet too large: fragmentation fields (32 bits)

## Slide 18: Preventing loops (TTL)
Forwarding loops cause packets to cycle for a long time
  Left unchecked would accumulate to consume all capacity
Time-to-Live (TTL) Field (8 bits)
  Decremented at each hop; packet discarded if 0
    “Time exceeded” message is sent to the source

## Slide 19: Header corruption (Checksum)
Checksum (16 bits)
  Particular form of checksum over packet header
If not correct, router discards packets
  So it doesn’t act on bogus information
Checksum recalculated at every router
  Why?
Notes: TTL

## Slide 20: Fragmentation
Every link has a “Maximum Transmission Unit” (MTU)
  Largest number of bits it can carry as one unit
A router can split a packet into multiple “fragments” if the packet size exceeds the link’s MTU
Must reassemble to recover original packet
Will return to fragmentation later …

## Slide 21: What information do we need?
Parse packet
  IP version number (4 bits), packet length (16 bits)
Carry packet to the destination
  Destination’s IP address (32 bits)
Deal with problems along the way
  TTL (8 bits), checksum (16 bits), frag. (32 bits)
Accommodate evolution
  Version number (4 bits) (+ fields for special handling)
Specify any special handling

## Slide 22: Special handling
“Type of Service” (8 bits)
  Allow packets to be treated differently based on needs
    e.g., indicate priority, congestion notification
  Has been redefined several times
  Now called “Differentiated Services Code Point (DSCP)”

## Slide 23: Options
Optional directives to the network
  Not used very often
  16 bits of metadata + option-specific data
Examples of options
  Record Route
  Strict Source Route
  Loose Source Route
  Timestamp

## Slide 24: What information do we need?
Parse packet
  IP version number (4 bits), packet length (16 bits)
Carry packet to the destination
  Destination’s IP address (32 bits)
Deal with problems along the way
  TTL (8 bits), checksum (16 bits), frag. (32 bits)
Accommodate evolution
  Version number (4 bits) (+ fields for special handling)
Specify any special handling
  ToS (8 bits), Options (variable length)

## Slide 25: IP packet structure
4-bit
Version
4-bit
Header
Len
8-bit
ToS
16-bit
Total Length (Bytes)
16-bit
Header Checksum
8-bit
TTL
32-bit
Destination IP Address
Options (if any)
Payload

## Slide 26: Parse packet
Header length (4 bits)
  Number of 32-bit words in the header
  Typically “5” (for a 20-byte IPv4 header)
  Can be more when IP options are used

## Slide 27: IP packet structure
4-bit
Version
4-bit
Header
Len
8-bit
ToS
16-bit
Total Length (Bytes)
16-bit
Header Checksum
8-bit
TTL
32-bit
Destination IP Address
Options (if any)
For Fragmentation

## Slide 28: Tasks at the destination end-system
Tell destination what to do with the received packet
Get responses to the packet back to the source

## Slide 29: Telling end-host how to handle packet
Protocol (8 bits)
  Identifies the higher-level protocol
  Important for de-multiplexing at receiving host
Application
Transport
Network
Data link
Physical
L7
L4
L3
L2
L1
SMTP
HTTP
TCP
UDP
IP
PPP
FDDI
Ethernet
PSTN
Radio
Copper
Optical
NTP
DNS

## Slide 30: Telling end-host how to handle packet
Protocol (8 bits)
  Identifies the higher-level protocol
  Important for de-multiplexing at receiving host
Most common examples
  E.g., “6” for the Transmission Control Protocol (TCP)
  E.g., “17” for the User Datagram Protocol (UDP)
IP header
IP header
TCP header
UDP header
protocol=6
protocol=17

## Slide 31: Tasks at the destination end-system
Tell destination what to do with the received packet
  Transport layer protocol (8 bits)
Get responses to the packet back to the source
  Source IP address (32 bits)

## Slide 32: IP packet structure
4-bit
Version
4-bit
Header
Len
8-bit
ToS
16-bit
Total Length (Bytes)
16-bit
Header Checksum
8-bit
TTL
32-bit
Destination IP Address
Options (if any)
For Fragmentation
8-bit
Protocol
32-bit
Source IP Address

## Slide 33: Dealing with fragmentation

## Slide 34: A closer look at fragmentation
Every link has a “Maximum Transmission Unit” (MTU)
  Largest number of bits it can carry as one unit
A router can split a packet into multiple “fragments” if the packet size exceeds the link’s MTU
Must reassemble to recover original packet

## Slide 35: Example of fragmentation
A 4000 byte packet crosses a link w/ MTU=1500B
4000B
1500B
…

## Slide 36: Example of fragmentation
A 4000 byte packet crosses a link w/ MTU=1500B
20
4000
3980
20
1480
1500
20
1200
1220
20
1300
1320
IP header

## Slide 37: Why reassemble?
20
4000
3980
20
1480
1500
20
1200
1220
20
1300
1320
IP header
20
TCP
TCP
TCP
HTTP
HTTP
HTTP
Must reassemble before sending packet to higher layers!

## Slide 38: A few considerations
Where to reassemble?
Fragments can get lost
Fragments can follow different paths
Fragments can get fragmented again

## Slide 39: Where should reassembly occur?
Classic case of E2E principle
At next-hop router imposes burden on network
  Complicated reassembly algorithm
  Must hold onto fragments/state
Any other router may not work
  Fragments may take different paths
Little benefit, large cost for network reassembly
Hence, reassembly is done at the destination

## Slide 40: Reassembly: What fields?
Need a way to identify fragments of the packet
  Introduce an identifier
Fragments can get lost
  Need some form of sequence number or offset
Sequence numbers / offset
  How do I know when I have them all? (need max seq# / flag)
  What if a fragment gets re-fragmented?

## Slide 41: IPv4’s fragmentation fields
Identifier: which fragments belong together
Flags:
  Reserved: ignore
  DF: don’t fragment
    May trigger error message back to sender
  MF: more fragments coming
Offset: portion of original payload this fragment contains
  In 8-byte units

## Slide 42: IP packet structure
4-bit
Version
4-bit
Header
Len
8-bit
ToS
16-bit
Total Length (Bytes)
16-bit
Identification
13-bit
Fragment Offset
3-bit
Flags
16-bit
Header Checksum
8-bit
Protocol
8-bit
TTL
32-bit
Source IP Address
32-bit
Destination IP Address
Options (if any)
For Fragmentation

## Slide 43: Why this works
Fragment without MF set (last fragment)
  Tells host which are the last bits in original payload
All other fragments fill in holes
Can tell when holes are filled, regardless of order
  Use offset field
Q: why use a byte-offset for fragments rather than numbering each fragment?
  Allows further fragmentation of fragments

## Slide 44: Example of fragmentation (contd.)
Packet split into 3 pieces
Example:
20
4000
3980
20
1480
1500
20
1200
1220
20
1300
1320

## Slide 45: Example of fragmentation, contd.
4000 byte packet from host 1.2.3.4 to 5.6.7.8 traverses a link with MTU 1,500 bytes
(3980 more bytes of payload here)
Version
4
Header
Len
5
ToS
0
Total Length (Bytes)
4000
Identification
56273
Fragment Offset
0
R/D/M
0/0/0
Header Checksum
44019
Protocol
6
TTL
127
Source IP Address
1.2.3.4
Destination IP Address
5.6.7.8

## Slide 46: Example of fragmentation, contd.
Datagram split into 3 pieces. Possible first piece:
Version
4
Header
Len
5
ToS
0
Total Length (Bytes)
1500
Identification
56273
Fragment Offset
0
R/D/M
0/0/1
Header Checksum
xxx
Protocol
6
TTL
127
Source IP Address
1.2.3.4
Destination IP Address
5.6.7.8

## Slide 47: Example of fragmentation, contd.
Possible second piece: Frag#1 covered 1480bytes
Version
4
Header
Len
5
ToS
0
Total Length (Bytes)
1220
Identification
56273
Fragment Offset
185 (185 * 8 = 1480)
R/D/M
0/0/1
Header Checksum
yyy
Protocol
6
TTL
127
Source IP Address
1.2.3.4
Destination IP Address
5.6.7.8

## Slide 48: Example of fragmentation, contd.
Possible third piece: 1480+1200 = 2680
Version
4
Header
Len
5
ToS
0
Total Length (Bytes)
1320
Identification
56273
Fragment Offset
335 (335 * 8 = 2680)
R/D/M
0/0/0
Header Checksum
zzz
Protocol
6
TTL
127
Source IP Address
1.2.3.4
Destination IP Address
5.6.7.8

## Slide 49: A quick look into IPv6

## Slide 50: IPv6
Motivated (prematurely) by address exhaustion
  Addresses four times as big (128-bit)
Focused on simplifying IP
  Got rid of all fields that were not absolutely necessary
Result is an elegant, if unambitious, protocol

## Slide 51: What “clean up” would you do?
4-bit
Version
4-bit
Header
Len
8-bit
ToS
16-bit
Total Length (Bytes)
16-bit
Identification
13-bit
Fragment Offset
3-bit
Flags
16-bit
Header Checksum
8-bit
Protocol
8-bit
TTL
32-bit
Source IP Address
32-bit
Destination IP Address
Options (if any)
Payload

## Slide 52: IPv4 and IPv6 header comparison
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
128-bit Source Address |  |  |  | 
128-bit Destination Address |  |  |  | 
IPv4
IPv6
Field name kept from IPv4 to IPv6
Fields not kept in IPv6
Name & position changed in IPv6
New field in IPv6

## Slide 53: Summary of changes
Eliminated fragmentation (why?)
Eliminated checksum (why?)
New options mechanism (why?)
Eliminated header length (why?)
Expanded addresses
Added Flow Label

## Slide 54: Philosophy of changes
Don’t deal with problems: leave to ends
  Eliminated fragmentation and checksum
  Why retain TTL?
Simplify handling:
  New options mechanism (uses next header)
  Eliminated header length
    Why couldn’t IPv4 do this?
Provide general flow label for packet
  Not tied to semantics
  Provides great flexibility

## Slide 55: Summary
Network layer can be divided into data plane and control plane
  Data plane deals with “how?”
  Control plane deals with “what?”
IP is simple yet nuanced