## Slide 1: CSCI4430 Computer Networks Lecture12: Network Layer – Routing fundamentals
Hong Xu, Henry
CSE@CUHK, 2023
Material with thanks to Patrick Lee, Mosharaf Chowdhury, Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Goal of routing
Find a path to a given destination
How do we know that the state contained in forwarding tables meets our goal?
  This is what “validity” of routing state tells us
  [This is non-standard terminology]

## Slide 3: Local vs. global view of state
Local routing state is the forwarding table in a single router
  By itself, the state in a single router cannot be evaluated
  It must be evaluated in terms of the global context

## Slide 4: Example: Local vs. global view of state
111010010
MIT
#1
#2
#3
#4
Dst | Next Hop
UMICH | 1
UCB | 3
MIT | 2
NYU | 4
#0
Forwarding Table @ #0
To UMich
To MIT
To UCB
To NYU
Dst | Next Hop
UMICH | 0
UCB | 0
MIT | 0
NYU | 0
Forwarding Table @ #6
#6
Dst | Next Hop
UMICH | 0
UCB | 0
MIT | 
NYU | 0
Forwarding Table @ #2

## Slide 5: Local vs. global view of state
Local routing state is the forwarding table in a single router
  By itself, the state in a single router cannot be evaluated
  It must be evaluated in terms of the global context
Global state refers to the collection of forwarding tables in each of the routers
  Global state determines which paths packets take
  (Will discuss later where this routing state comes from)

## Slide 6: “Valid” routing state
Global state is “valid” if it produces forwarding decisions that always deliver packets to their destinations
Goal of routing protocols: compute valid state
  How can we tell if routing state if valid?
Need a succinct correctness condition for routing
Notes: What could go wrong?

## Slide 7: Necessary and sufficient condition
Global routing state is valid if and only if:
  There are no dead ends (other than destination)
  There are no loops
A dead end is when there is no outgoing link (next-hop)
  A packet arrives, but the forwarding decision does not yield any outgoing link
A loop is when a packet cycles around the same set of nodes forever

## Slide 8: Loop!
111010010
MIT
#1
#2
#3
#4
Dst | Next Hop
UMICH | 1
UCB | 3
MIT | 2
NYU | 4
#0
Forwarding Table @ #0
To UMich
To MIT
To UCB
To NYU
Dst | Next Hop
UMICH | 0
UCB | 0
MIT | 0
NYU | 0
Forwarding Table @ #6
#6
Dst | Next Hop
UMICH | 0
UCB | 0
MIT | 0
NYU | 0
Forwarding Table @ #2

## Slide 9: Dead end to MIT @ #0
111010010
MIT
#1
#2
#3
#4
Dst | Next Hop
UMICH | 1
UCB | 3
NYU | 4
#0
Forwarding Table @ #0
To UMich
To MIT
To UCB
To NYU
Dst | Next Hop
UMICH | 0
UCB | 0
MIT | 0
NYU | 0
Forwarding Table @ #6
#6
Dst | Next Hop
UMICH | 0
UCB | 0
MIT | 0
NYU | 0
Forwarding Table @ #2

## Slide 10: Necessary and sufficient condition
Global routing state is valid if and only if:
  There are no dead ends (other than destination)
  There are no loops

## Slide 11: Necessary (“only if”)
If you run into a dead end before hitting destination,
  you’ll never reach the destination
If you run into a loop,
  you’ll never reach destination

## Slide 12: Sufficient (“if”)
Assume there are no dead ends and no loops
Packet must keep wandering, but without repeating
  If ever enter same switch from same link, will loop
Only a finite number of possible links for it to visit
  It cannot keep wandering forever without looping
  Must eventually hit destination
Notes: Destination is only safe deadend

## Slide 13: Checking validity of routing state
Focus only on a single destination
  Ignore all other routing state
Mark outgoing link (“next hop”) with arrow
  There is only one at each node
Eliminate all links with no arrows
Look at what’s left

## Slide 14: Example 1

## Slide 15: Pick a destination

## Slide 16: Put arrows on outgoing links (to green dot)

## Slide 17: Remove unused links
Leaves spanning tree: Valid

## Slide 18: Example 2
Is this valid?

## Slide 19: Not valid: Contains loop!

## Slide 20: Routing validity
Very easy to check validity of routing state for a particular destination
Dead ends are nodes without outgoing arrow
Loops are obvious too
  Disconnected from rest of graph

## Slide 21: Goal of routing
v1: Find a path to a given destination
v2: Find a least-cost path to a given destination

## Slide 22: Example
dest.
next hop
z
?
4
1
2
v
u
z
v
?
link costs
Could represent
Propagation delay
Load
Cost
dest.
next hop
u
?
v
?
dest.
next hop
z
?
u
?
Notes: (First example, link costs.)
Let’s suppose that there are only 3 routers in the entire Internet,
and they are all directly connected to each other in this triangle.
For each router, we will decide how it should reach every other router.
For example, router u can reach router z directly,
or it can reach router z indirectly, through router v.
Which of the two routes (paths) is better?
In other words, for each source router,
we will decide which is the best next hop to every destination router.
How will we decide? We will rely on these 3 clicks things called click “link costs”.
Each link is associated with a link cost.
The lower the link cost, the better the quality of the link.
So, link costs could represent, for example,
click the propagation delay of the link,
or its click current load.

## Slide 23: Example
4
1
2
v
u
z
least-cost path from u to z:
u v z
least cost path from u to v:
u v
v
v
v
v
dest.
next hop
z
u
u
z
dest.
next hop
z
dest.
next hop
u
v
v
Notes: (Least-cost routing.)
For each pair of routers, we will find the path that has the least total cost.
For example, from source router click u to destination router z,
- there is the click direct path, which has cost 4;
- and the click indirect one, through v, which has cost 1 + 2 = 3.
So, the click indirect one is the best path.
Now, let’s fill in the forwarding table of router u:
- the best next hop to destination router z is click router v.
click
Similarly, from click source router u to destination router v,
- there is a click direct path, of cost 1;
- and an click indirect one, through z, of cost 4 + 2 = 6.
So, the best path is the direct one.
Now, let’s fill in the forwarding table of router u:
- the best next hop to destination router v is click router v itself.
click
In a similar manner, we can fill in the forwarding tables of routers 2 clicks z and 2 clicks v.

## Slide 24: Least-cost path routing
Given: router graph & link costs
Goal: find least-cost path
  From each source router to each destination router

## Slide 25: Least-cost routes
Least-cost routes provide an easy way to avoid loops
  No reasonable cost metric is minimized by traversing a loop
Least-cost paths form a spanning tree for each destination rooted at that destination

## Slide 26: Dijkstra’s algorithm
Network topology, link costs known to all nodes
  All nodes have same info
Computes least-cost paths from one node (“src”) to all other nodes
  After k iterations, know least-cost path to k destinations
Notations
  c(x,y): link cost from x to y;
    ∞ if not direct neighbors
  D(v): current cost of path from src to v
  p(v): predecessor node along path from src to v
  N‘: set of nodes whose least-cost path are definitively known

## Slide 27: Dijkstra’s algorithm
1 Initialization:
2 N' = {u}; D(u) = 0
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞

## Slide 28: Dijkstra’s algorithm
1 Initialization:
2 N' = {u}; D(u) = 0
3 for all nodes v
4 if v adjacent to u
5 then D(v) = c(u,v)
6 else D(v) = ∞
7
8 Loop
9 find w not in N' such that D(w) is a minimum
10 add w to N'
11 update D(v) for all v adjacent to w and not in N':
12 D(v) = min( D(v), D(w) + c(w,v) )
13 /* new cost to v is either old cost to v or known
14 least path cost to w plus cost from w to v */
15 until all nodes are in N'

## Slide 29: Dijkstra’s algorithm: Example
3
4
5
3
7
4
8
2
7
9
x
u
z
v
y
w
Step
N'
D(v)
p(v)
0
1
2
3
4
5
D(w)
p(w)
D(x)
p(x)
D(y)
p(y)
D(z)
p(z)
u
∞
∞
7,u
3,u
5,u
uw
∞
11,w
6,w
5,u
14,x
11,w
6,w
uwx
uwxv
14,x
10,v
uwxvy
12,y
Notes:
Construct shortest path tree by tracing predecessor nodes
Ties can exist (can be broken arbitrarily)
uwxvyz

## Slide 30: Dijkstra’s algorithm: Example
3
5
3
4
2
x
u
z
v
y
w
Resulting least-cost tree
from u
Resulting forwarding table
in u
v
w
x
y
z
(u, w)
(u, w)
(u, x)
(u, w)
(u, w)
destination
link

## Slide 31: Dijkstra’s algorithm
Why does it work?
If P is a node on the minimum-cost path from S to D, then the sub-path from S to P is also the minimum-cost path from S to P.
Bellman’s ‘principle of optimality’ in dynamic programming

## Slide 32: Summary
Network layer control plane calculates valid routes and sets up forwarding table
  Avoiding loops and dead ends
Least-cost routes can be calculated using Dijkstra’s algorithm
Next lecture: Routing protocols