## Slide 1: ESTR4120 Computer Networks Lecture 3: CDN, Anycast
Hong Xu
Materials from Girish Borkar’s CISC 856 slides at University of Delaware

## Slide 2: More on CDN

## Slide 3: Slow Access Time Problem World Wide Wait
Public Internet
Client Access Network
Server Access Network
CNN
network
eecis
ren.cis
CNN.com
low bandwidth link
congested link
overloaded

## Slide 4: Server Farm
L4-L7 Switch
Does load balancing
Internet
Server-1
Server-2
Server-n
Requests = R
Requests = R/n

## Slide 5: Client Network without a Web Cache
1.5 Mbps access link
100 Mbps LAN
Internet delay=2 sec
15 requests/sec
Avg. object size = 100 Kbits
Access delay =
ΔLAN = 15x100 Kb/100 Mbps = 0.015
Δaccess link = 15x100 Kb/1.5 Mbps = 1
Δ – traffic intensity
HUGE
Total delay =
Internet delay +
Access delay

## Slide 6: Web Cache: Basic operation
GET
Object present ?
No-> Fetch Object
Yes-> Send Object
GET
RESPONSE
Cache
RESPONSE
GET
RESPONSE
Client 1
Web server

## Slide 7: Web Cache
1.5 Mbps access link
100 Mbps LAN
Internet delay=2 Sec
delay = tens of milliseconds
ΔAL = 0.6
Δ – traffic intensity
Institutional
cache
Hit rate = 0.4
Total delay =
(2 + .01) x 0.6 = 1.2 Sec

## Slide 8: Content Distribution Network of Caches
Web server
Web server
Proactive replication
Parent
Child 1
Child 2

## Slide 9: Problems with discussed approaches: Server farms and Caching proxies
Server farms do nothing about problems due to network congestion, or to improve latency issues due to the network
Caching proxies serve only their clients, not all users on the Internet
Content providers (say, Web servers) cannot rely on existence and correct implementation of caching proxies
Accounting issues with caching proxies.
For instance, www.cnn.com needs to know the number of hits to the advertisements displayed on the webpage.

## Slide 10: CDN: Basic Idea
congested
Not congested
original content
Replica
Replica
Client

## Slide 11: Content Distribution Networks
A mechanism for
replicating content on multiple servers on the Internet.
providing clients with a means to determine the servers that can deliver the content fastest.

## Slide 12: Terminology
Content: Any publicly accessible combination of text, images, applets, frames, MP3, video, flash, virtual reality objects, etc.
Content Provider: Any individual, organization, or company that has content that it wishes to make available to users.
Origin Server: Content providers server , where the content is first uploaded.
Surrogate Server: Content distributor’s server, where the replicated content is kept.

## Slide 13: Players of the game
Content Provider
H/W and S/W
Vendor
Content
Distributor
Hosting
Provider
Yahoo,
MSNBC,
CNN
Cisco,
Lucent,
Inktomi,
CacheFlow
Akamai,
Digital Island,
AT&T
Exodus
Sells servers
Send content
Install servers

## Slide 14: CDN: Distribution
CDN server in Asia
CDN server in
Europe
CDN server in South
America
CDN distribution node
Origin server in
North America
push
content
push content
push content
push content
Akamai CDN

## Slide 15: CDN: Functional Components
Distribution Service
Redirection Service
Accounting and Billing system

## Slide 16: CDN: Architecture
Request
Routing
Infrastructure
Distribution
and
Accounting
Infrastructure
CDN
Client
Surrogate
Surrogate
Origin

## Slide 17: CDN: Request Routing Mechanisms
Best surrogate selected based on some metrics.
Techniques
  DNS based request routing
  Content Modification (URL rewriting)
  Anycast based
  Transport layer request routing
  Combination of multiple mechanisms

## Slide 18: CDN: DNS based Request Routing
Akamai DNS
Local DNS Server
128.4.4.12
www.cnn.com
63.251.132.22
www.cnn.com
63.251.132.22
Session
63.251.132.22
63.210.135.39
surrogate
surrogate
www.cnn.com
ping
ping
Measure to client DNS
Results

## Slide 19: Content Modification
...
<img src="http://www.cdn.com/cnn/images/1.gif”>
...
Index.html
GET www.cnn.com/index.html
Index.html
DNS query: cdn.com ?
GET /cnn/images/1.gif
1.gif
64.236.24.28
Authoritative DNS server for cdn.com
Local DNS server
Client
CNN.com
64.236.24.28
DNS query: cdn.com ?
64.236.24.28
PUT /images/*.gif

## Slide 20: Metrics
Network Proximity (Surrogate to Client):
  Network hops (traceroute)
  RTT
  Internet mapping services (NetGeo, IDMaps)
  …
Surrogate Load:
  Number of active TCP connections
  HTTP request arrival rate
  Other OS metrics
  …
Bandwidth Availability

## Slide 21: Full site delivery vs. Partial Site Delivery
Full Site Delivery : All the contents are delivered by the CDN (including HTML, images, and other objects).
Partial Site delivery: Only images, streaming media and other bandwidth intensive objects delivered by the CDN.

## Slide 22: Content Distribution Internetworking: CDI
Interconnection of Content Networks – collaboration between caching proxies and CDNs, as well as between individual CDNs
Greater reach, larger scale, higher capacity, increased fault tolerance
Basic architecture involves gateways between various content networks

## Slide 23: CDI: Architecture
comcast
Akamai
ATT
Digital Island
Cache network
Content Peering Gateway

## Slide 24: CDN vs. Caching Proxies
Caching Proxies | CDN
Used by ISP to reduce bandwidth consumption. | Used by Content Providers to increase QoS.
Operate Reactively | Operate Proactively
Caching proxies cater to their users (web clients) and not to content providers (web servers) | CDNs cater to the content providers (web servers) and clients
Caching proxies do not give control of the content to the content providers. | CDNs do

## Slide 25: Anycast [RFC4786]

## Slide 26: What’s anycast?
One of the major routing schemes
  One-to-one: unicast, anycast
  One-to-many: multicast, broadcast
Unicast is what we’ve assumed
  Only one destination in the entire network
For anycast, one destination address, but many potential destinations
  The network picks the actual destination and the route that is most preferred
  Service address, instead of machine address

## Slide 27: How does it work?
In the WAN level, done over BGP
Each router announces the same (external-facing) IP with different routes
Router chooses the ”shortest” path when routing packets with that IP
Same IP (CloudFlare)
From San Francisco
From London

## Slide 28: Why use anycast? Who uses it?
Load balancing and failover; transparent to users
  If a path or a data center fails, just route to the other servers
  Select a destination closer to the user
Use routing protocol to LB is more resilient than using hardware boxes
Widely used in DNS and CDN
  DNS root servers: a cluster of servers with anycast to provide service with the same root server IP (but closer to user)
  Suitable for UDP traffic

## Slide 29: Additional material
Building and operating a global DNS anycast network, slides by Gael Hernandez from PCH