## Slide 1: CSCI4430 Computer Networks Lecture 4: Application Layer – Caching and CDN, DNS
Hong Xu, Henry
CSE@CUHK, 2022
Material with thanks to Patrick Lee, Mosharaf Chowdhury, Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Agenda
Caching
CDN: Content Distribution Network
DNS: Domain Name System

## Slide 3: Recap: Improving HTTP performance
Optimizing connections using three “P”s
  Persistent (latency)
  Parallel/concurrent (bandwidth and latency)
  Pipelined over the same connection (latency)
Caching
  Forward proxy: close to clients
  Reverse proxy: close to servers
Replication

## Slide 4: Caching
Why does caching work?
  Exploits locality of reference
How well does caching work?
  Very well, up to a limit
  Large overlap in content
  But many unique requests
    A universal story!
    Effectiveness grows logarithmically in size

## Slide 5: Caching: How
Modifier to GET requests:
  If-modified-since – returns “not modified” if resource not modified since specified time
GET /somedir/page.html HTTP/1.1
Host: www.someschool.edu
User-agent: Mozilla/4.0
If-modified-since: Wed, 18 Jan 2017 10:25:50 GMT
(blank line)

## Slide 6: Caching: How
Modifier to GET requests:
  If-modified-since – returns “not modified” if resource not modified since specified time
Client specifies “if-modified-since” time in request
Server compares this against “last modified” time of resource
Server returns “Not Modified” if resource has not changed
…. or a “OK” with the latest version otherwise

## Slide 7: Caching: How
Modifier to GET requests:
  If-modified-since – returns “not modified” if resource not modified since specified time
Response header:
  Expires – how long it’s safe to cache the resource
  No-cache – ignore all caches; always get resource directly from server

## Slide 8: Caching: Where?
Options
  Client (browser)
  Forward proxies
  Reverse proxies
  Content Distribution Network

## Slide 9: Caching: Where?
Many clients request the same content
  E.g., cuhk; youtube videos; software updates
  Generate unnecessary server and network load
  Clients experience unnecessary latency
Server
Clients
Tier-1 ISP
ISP-1
ISP-2

## Slide 10: Caching with Reverse Proxies
Cache documents close to server
  Decrease server load
  By content provider
10
Clients
Tier-1 ISP
ISP-1
ISP-2
Reverse proxies

## Slide 11: Caching with Forward Proxies
Cache documents close to clients
  Reduce network traffic and decrease latency
  By ISPs or enterprises
11
Clients
Tier-1 ISP
ISP-1
ISP-2
Reverse proxies
Forward proxies

## Slide 12: Replication
Replicate popular websites across many machines
  Spreads load across servers
  Places content closer to clients
  Helps when content isn’t cacheable

## Slide 13: Content Distribution Networks (CDN)
Caching and replication as a service
Large-scale distributed storage infrastructure (usually) administered by one entity
  e.g., Akamai is in 130 countries and 1400 networks
  [demo]
Combination of caching and replication
  Pull: Direct result of clients’requests (caching)
  Push: Expectation of high access rate (replication)
Notes: Transcoding = change compression rate per user’s bandwidth

## Slide 14: Cost-effective content delivery
General theme: multiple sites hosted on shared physical infrastructure
  Efficiency of statistical multiplexing
  Economies of scale (volume pricing, etc.)
  Amortization of human operator costs
Examples:
  CDNs
  Web hosting companies
  Cloud infrastructure

## Slide 15: CDN example – Akamai
Akamai creates new domain names for each client
  e.g., a128.g.akamai.net for cnn.com
The client content provider modifies content so that embedded URLs reference new domains
  “Akamaize” content
  e.g., http://www.cnn.com/image-of-the-day.gif becomes http://a128.g.akamai.net/image-of-the-day.gif
Requests now sent to CDN’s infrastructure

## Slide 16: CDN example – Akamai
Retrieved on Sep 10, 2021 from https://www.akamai.com/visualizations/media-delivery-network-map

## Slide 17: Why direct clients to particular replicas?
Balancing load across server replicas
Pairing clients with nearby servers to decrease latency and overall bandwidth usage

## Slide 18: DNS: Domain name system

## Slide 19: Internet names & addresses
Machine addresses: e.g., 141.212.113.143
  Router-usable labels for machines
  Conforms to network structure (the “where”)
Machine names: e.g., cse.cuhk.edu.hk
  Human-usable labels for machines
  Conforms to organizational structure (the “who”)
The Domain Name System (DNS) is how we map from one to the other
  A directory service

## Slide 20: Why?
Convenience
  Easier to remember
Provides a level of indirection!
  Decoupled names from addresses
  Many uses beyond just naming a specific host

## Slide 21: DNS: History
Initially all host-address mappings were in a hosts.txt file (in /etc/hosts):
  Maintained by the Stanford Research Institute (SRI)
  Changes were submitted by email and updates downloaded periodically from SRI
As the Internet grew SRI could not handle load
  Names were not unique anymore
  Hosts had inaccurate copies of hosts.txt

## Slide 22: DNS: History
In 1983, the first stable operational DNS implementation included
  The associated query protocol;
  A server implementation; and
  Initial root servers.
Since inception, DNS scaled from 1000s of queries/day to 10s of billions queries/day

## Slide 23: Goals
Uniqueness: no naming conflicts
Scalable
  Many names and frequent updates (secondary)
Distributed, autonomous administration
  Ability to update my own (machines’) names
  Don’t have to track everybody’s updates
Highly available
Lookups are fast
Perfect consistency is a non-goal

## Slide 24: How?
Partition the namespace
Distribute administration of each partition
  Autonomy to update my own (machines’) names
  Don’t have to track everybody’s updates
Distribute name resolution for each partition
How should we partition things?

## Slide 25: Key idea: Hierarchy
Three intertwined hierarchies
  Hierarchical namespace
    As opposed to original flat namespace
  Hierarchically administered
    As opposed to centralized
  (Distributed) hierarchy of servers
    As opposed to centralized storage

## Slide 26: Hierarchical namespace
“Top Level Domains” are at the top
Domains are subtrees
  e.g., .edu, umich.edu, eecs.umich.edu
Name is leaf-to-root path
  cse.eecs.umich.edu
Depth of tree is arbitrary (limit 128)
Name collisions trivially avoided
  Each domain is responsible
root
edu
com
gov
mil
org
net
cn
fr
umich
berkeley
eecs
law
cse
…

## Slide 27: Hierarchical administration
root
edu
com
gov
mil
org
net
cn
fr
umich
berkeley
eecs
law
cse
…
A zone corresponds to an administrative authority that is responsible for that portion of the hierarchy
  e.g., UMich controls names: *.umich.edu
  e.g., EECS controls names: *.eecs.umich.edu
ICANN/IANA
Notes: ICANN: Internet Corporation for Assigned Names and Numbers
IANA: Internet Assigned Numbers Authority

## Slide 28: Server hierarchy
Top of hierarchy: Root servers
  Location hardwired into other servers
Next Level: Top-level domain (TLD) servers
  .com, .edu, etc.
  Managed professionally
Bottom Level: Authoritative DNS servers
  Actually store the name-to-address mapping
  Maintained by the corresponding administrative authority

## Slide 29: Server hierarchy
Each server stores a (small!) subset of the total DNS database
An authoritative DNS server stores “resource records” for all DNS names in the domain that it has authority for
Each server needs to know other servers responsible for other portions of the hierarchy
  Every server knows the root
  Root server knows about all top-level domains

## Slide 30: DNS root
Located in Virginia, USA
How do we make the root scale?

## Slide 31: 13 DNS root servers
https://root-servers.org/

## Slide 32: Root servers
https://www.iana.org/domains/root/servers
13 root servers, many instance for each
A Cisco 7301 router and a Juniper M7i, part of the K root-server instance at AMS-IX
Credit: https://commons.wikimedia.org/wiki/File:Ams-ix.k.root-servers.net.jpg

## Slide 33: Start assignment 1 asap!

## Slide 34: DNS records
DNS servers store resource records (RRs)
  RR is (name, value, type, TTL)
Type = A: ( Address)
  name = hostname
  value = IP address
Type = NS: ( Name Server)
  name = domain
  value = name of DNS server for domain

## Slide 35: DNS records (cont’d)
Type = CNAME: ( Canonical Name)
  name = alias name for some “canonical” (real) name
    e.g., cse.umich.edu is really cse.eecs.umich.edu
  value = canonical name
Type = MX: ( Mail eXchanger)
  name = domain in email address
  value = name(s) of mail server(s)

## Slide 36: Inserting Resource Records
Register foobar.com at registrar
  Provide registrar with names and IP addresses of your authoritative name server(s)
  Registrar inserts RR pairs into the .com TLD server:
    (foobar.com, dns1.foobar.com, NS)
    (dns1.foobar.com, 212.44.9.129, A)
Store resource records in your server dns1.foobar.com
  e.g., type A record for www.foobar.com
  e.g., type MX record for foobar.com

## Slide 37: Using DNS (Client/App View)
Two components
  Local DNS servers
  Resolver software on hosts
Local DNS server (“default name server”)
  Clients configured with default server’s address OR learn it via a host configuration protocol (e.g., DHCP)
Client application
  Obtain DNS name (e.g., from URL)
  Do getnameinfo() to trigger DNS request to its local DNS server
Notes: DHCP: Dynamic Host Configuration Protocol

## Slide 38: dig
dig nyu.edu
; <<>> DiG 9.10.6 <<>> nyu.edu
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 47443
;; flags: qr rd ra; QUERY: 1, ANSWER: 1, AUTHORITY: 0, ADDITIONAL: 1
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags:; udp: 512
;; QUESTION SECTION:
;nyu.edu. IN A
;; ANSWER SECTION:
nyu.edu. 60 IN A 216.165.47.10
;; Query time: 39 msec
;; SERVER: 192.168.1.1#53(192.168.1.1)
;; WHEN: Fri Sep 10 08:21:43 EDT 2021
;; MSG SIZE rcvd: 52

## Slide 39: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers

## Slide 40: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 41: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 42: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 43: Name resolution: Recursive
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 44: Name resolution: Iterative
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?

## Slide 45: Two ways to resolve a name
Recursive name resolution
  Ask server to do it for you
Iterative name resolution
  Ask server who to ask next
The iterative example we saw is a mix of both!

## Slide 46: DNS protocol
Query and Reply messages; both with the same message format
  Header: identifier, flags, etc.
  Plus resource records
Client-server interaction on UDP Port 53
  Spec supports TCP too, but not always implemented

## Slide 47: Goals: Are we there yet?
Uniqueness: No naming conflicts
Scalable
Distributed, autonomous administration
Highly available?

## Slide 48: Reliability
Replicated DNS servers (primary/secondary)
  Name service available if at least one replica is up
  Queries can be load-balanced between replicas
Usually, UDP used for queries
  Reliability, if needed, must be implemented on UDP
Try alternate servers on timeout
  Exponential backoff when retrying same server
Same identifier for all queries
  Don’t care which server responds

## Slide 49: Goals: Are we there yet?
Uniqueness: No naming conflicts
Scalable
Distributed, autonomous administration
Highly available
Fast lookups?

## Slide 50: DNS caching
Performing all these queries takes time
  Up to 1-second latency before starting download
Caching can greatly reduce overhead
  The top-level servers very rarely change
  Popular sites (e.g., www.google.com) visited often
  Local DNS server often has the information cached
How DNS caching works
  DNS servers cache responses to queries
  Responses include a “time to live” (TTL) field
  Server deletes cached entry after TTL expires

## Slide 51: TTL in dig output
dig nyu.edu
; <<>> DiG 9.10.6 <<>> nyu.edu
;; global options: +cmd
;; Got answer:
;; ->>HEADER<<- opcode: QUERY, status: NOERROR, id: 47443
;; flags: qr rd ra; QUERY: 1, ANSWER: 1, AUTHORITY: 0, ADDITIONAL: 1
;; OPT PSEUDOSECTION:
; EDNS: version: 0, flags:; udp: 512
;; QUESTION SECTION:
;nyu.edu. IN A
;; ANSWER SECTION:
nyu.edu. 60 IN A 216.165.47.10
;; Query time: 39 msec
;; SERVER: 192.168.1.1#53(192.168.1.1)
;; WHEN: Fri Sep 10 08:21:43 EDT 2021
;; MSG SIZE rcvd: 52
TTL
Notes: 60 Seconds

## Slide 52: Negative caching
Remember things that do not work
  Misspellings like www.google.comm
  These can take a long time to fail the first time
  Good to remember that they do not work so the failure takes less time the next time around
Negative caching is optional
  Not widely implemented

## Slide 53: Important properties of DNS
Administrative delegation and hierarchy enables:
  Easy unique naming
  Reasonable trust model
  Caching increases scalability and performance

## Slide 54: DNS provides indirection
Addresses can change underneath
  Move www.cnn.com to 4.125.91.21
Name could map to multiple IP addresses
  Load-balancing (CDN)
  Reducing latency by picking nearby servers (CDN)
  Try out: dig google.com a few times
Multiple names for the same address
  E.g., many services (mail, www) on same machine
  E.g., aliases like www.cnn.com and cnn.com

## Slide 55: Summary
CDNs improve web performance
  Via replication and caching
  Good server selection
DNS allows us to go to webpages without having to memorize IP addresses
  Allows a level of indirection that enables many functionalities including CDN server selection