## Slide 1: CSCI4430 Computer Networks Lecture 3: Application Layer – Socket programming, HTTP
Hong Xu
Material with thanks to Patrick Lee, Mosharaf Chowdhury, Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Agenda
Socket programming
HTTP and the Web
Improving HTTP performance

## Slide 3: How to implement a network application?
Implementation of each protocol layer is located in either the user-space, kernel-space, or the device (hardware)
Physical
Device
Application
Transport
Network
Data Link
Kernel
User
Client/Server
Program

## Slide 4: How to implement a network application?
We need a “door” so that a network application can send/receive messages to/from the network
The door should appear between the user space and kernel space so that details of the kernel space can be hidden
Socket is the door!
Application
Transport
Kernel
User
Client/Server
Program
What is the interface?

## Slide 5: How to implement a network application?
A socket is a host-local, application-created, OS-controlled interface (a “door”) into which application process can both send and receive messages to/from another application process
  Similar to a file descriptor, which interfaces between an application and a file
One socket is tied to one application process (or thread)
  An application can create many processes (and hence sockets)
Client/Server
Program
Socket
Socket
Socket
TCP Control
UDP Control

## Slide 6: Socket programming
Socket API
introduced in BSD4.1 UNIX, 1981
explicitly created, used, released by apps
client/server paradigm
two types of transport service via socket API:
  unreliable datagram
  reliable, byte stream-oriented
Socket programming is to build client/server application that communicate using sockets

## Slide 7: Socket-programming using TCP
TCP service: reliable transfer of bytes from one process to another.
An application may view TCP a reliable, in-order pipe (or stream).
process
TCP with
buffers,
variables
socket
controlled by
application
developer
controlled by
operating
system
host or
server
process
TCP with
buffers,
variables
socket
controlled by
application
developer
controlled by
operating
system
host or
server
internet

## Slide 8: Socket programming using TCP
Before client contacts server:
  server process must first be running
  server must have created socket (door) that welcomes client’s contact
Client contacts server by:
  creating client-local TCP socket
  specifying IP address, port number of server process
  When client creates socket: client TCP establishes connection to server TCP
When contacted by client, server creates new TCP socket for server process to communicate with client
  allows server to talk with multiple clients
  source port numbers used to distinguish clients

## Slide 9: Socket programming with TCP
socket
bind
listen
accept
send/recv
close
socket
connect
send/recv
close
3-way handshake
TCP server
When a TCP server creates a socket, it needs to specify:
  Identifier of the socket
  Connection mode (TCP/UDP)
Analogous to when you open a file in C, you need to specify:
  location of the file
  access mode (e.g., read-only, write-only)
TCP client
Operations of socket programming in C/C++
share data
(TA will go through details)

## Slide 10: Programming stuff...client
Important System calls | 
Client side | Server side
socket() | 
bind()* | bind()
connect() | listen() and accept()
* means optional.
socket()
connect()
read()
write()
bind()
Client flow chart
Step (1). socket()
- Create a socket.
Step (2). bind() [optional]
- Assign the socket a port number.
- Skip this step and will have a random port number assigned.
Step (3). connect()
- Connect to the remote server.
- It is a blocking system call.
read() – to receive data.
write() – to send data.
close() – to close the socket

## Slide 11: Programming stuff...server
Important System calls | 
Client side | Server side
socket() | 
bind()* | bind()
connect() | listen() and accept()
socket()
listen()
read()
write()
bind()
Server flow chart
Step (1) & Step(2) [ you know them now. ]
Step (3). listen()
- It sets the port to be listening to incoming connections, for TCP only.
Step (4). accept()
- Accept incoming connections.
- A blocking system call.
accept()
read() – to receive data.
write() – to send data.
close() – to close the socket
* means optional.

## Slide 12: Programming stuff...accept()
socket()
listen()
read() & write()
bind()
Server flow chart
accept()
Socket FD
Socket FD
Socket FD
Socket FD
Accept FD
read() & write()
Accept FD
An interesting thing about accept() is the creation of a new file descriptor!
Application layer’s point of view.
Good! It provides each connection a new handler and we can distinguish every connection!
connection #1
connection #n
Transport layer’s point of view.
Well, for TCP, every FD points to an unique TCP control structure. It is a necessary for reliable data transfer!

## Slide 13: Programming stuff...complete flow?
socket()
listen()
bind()
Server flow chart
accept()
Application-layer code
connection is closed.
socket()
connect()
bind()
Client flow chart
Application-layer code
DONE!
close()
exit()
read()
&
write()
Limitation:
Only supports a single client!
New connection arrives

## Slide 14: Programming stuff...server parallelization
socket()
listen()
bind()
Server main
flow chart
accept()
Application-layer code
fork() or pthread_create()
connection is closed.
exit() or
pthread_exit()
child
parent
Server client-handler flow chart
New connection arrives

## Slide 15: Addressing processes
A server can run many processes (or threads), each serving a client
If I’m a client, how to identify a server process?
IP address of host may work, but many processes can be running on same host
Use (IP address, port number)
  Analogous to mailing a letter to a professor in a department:
    IP address is the address of the department
    Port number is the mail box of the professor

## Slide 16: Addressing processes
Identifier of a server process includes both IP address of the server host and port number.
Example port numbers:
  HTTP server: 80
  Mail server: 25
  See /etc/services on a Linux machine for more
to send HTTP message to www.cse.cuhk.edu.hk web server:
  IP address: 137.189.91.182
  Port number: 80

## Slide 17: Addressing processes
A server usually has a fixed port number so that clients know where to connect to.
  When a socket is created, a fixed port number is associated.
However, client’s port number is allocated on demand when a socket is created.
In summary, the IP address and the port number are together used to address a server process.

## Slide 18: Illustrations on Socket Use with TCP
Step 1: Server waits for clients’ connections (i.e., calling accept())
HTTP server
IP: 137.189.91.182
Port: 80
accept()
socket

## Slide 19: Illustrations on Socket Use with TCP
Step 2: Client makes a connection via connect().
HTTP server
IP: 137.189.91.182
Port: 80
accept()
socket
HTTP client
IP: 137.189.x.y
Port: 12345
connect()

## Slide 20: Illustrations on Socket Use with TCP
Step 3: Server creates a new TCP socket to serve the connection
HTTP server
IP: 137.189.91.182
Port: 80
accept()
socket
HTTP client
IP: 137.189.91.182, port 80
IP: 137.189.x.y, port 12345
IP: 137.189.91.182, port 80
IP: 137.189.x.y, port 12345
Connection is identified by
(server’s IP, server’s port,
client’s IP, client’s port)

## Slide 21: Illustrations on Socket Use with TCP
Step 4: Server can accept more connections…
HTTP server
IP: 137.189.91.182
Port: 80
accept()
socket
HTTP client
IP: 137.189.91.182, port 80
IP: 137.189.x.y, port 12345
IP: 137.189.91.182, port 80
IP: 137.189.x.y, port 12345
HTTP client
IP: 137.189.91.182, port 80
IP: 137.189.u.v, port 16876
IP: 137.189.91.182, port 80
IP: 137.189.u.v, port 16876

## Slide 22: HTTP and the web

## Slide 23: The Web: History
World Wide Web (WWW): a distributed database of “pages” linked through Hypertext Transport Protocol (HTTP)
  First HTTP implementation – 1990
    Tim Berners-Lee at CERN
  HTTP/0.9 – 1991
    Simple GET command for the Web
  HTTP/1.0 – 1992
    Client/server information, simple caching

## Slide 24: The Web: History (cont’d)
World Wide Web (WWW): a distributed database of “pages” linked through Hypertext Transport Protocol (HTTP)
  HTTP/1.1 – 1996
    Performance and security optimizations
  HTTP/2 – 2015
    Latency optimizations via request multiplexing over single TCP connection
    Binary protocol instead of text
    Server push

## Slide 25: The Web: History (cont’d)
World Wide Web (WWW): a distributed database of “pages” linked through Hypertext Transport Protocol (HTTP)
  HTTP/3 – TBA
    Built on top of QUIC, which is a user-space congestion control protocol on UDP
    Solves head-of-line (HOL) blocking problem in multiplexing over single TCP connection

## Slide 26: What does it consist of?
Who uses it?
Who provides the content?
How do they communicate?
How do we find the content?
How is the content organized?
How is it displayed?

## Slide 27: Web components
Infrastructure:
  Clients
  Servers (DNS, CDN, Datacenters)
Content:
  URL: naming content
  HTML: formatting content
Protocol for exchanging information: HTTP

## Slide 28: Why is there nothing about the network?
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
Clients
Servers
Switch

## Slide 29: What we want
http://123.xyz
123.xyz server
HTTP Request

## Slide 30: What we get
http://123.xyz
123.xyz server
Hello
HTTP Response

## Slide 31: URL: Uniform Record Locator
protocol://host-name[:port]/directory-path/resource
Extend the idea of hierarchical hostnames to include anything in a file system
  https://github.com/henryhxu/CSCI4430-ESTR4120/tree/2022_spring/lecture/lec1.pptx
  Extend to program executions as well…
  https://www.google.com/search?q=csci4430
  Server-side processing can be included in the name

## Slide 32: URL: Uniform Record Locator
protocol://host-name[:port]/directory-path/resource
  protocol: http, ftp, https, smtp, rtsp, etc.
  host-name: DNS name, IP address
  port: defaults to protocol’s standard port
    E.g., http: 80, https: 443
  directory path: hierarchical, reflecting file system
  resource: Identifies the desired resource

## Slide 33: Hyper Text Transfer Protocol (HTTP)
Client-server architecture
  Server is “always on” and “well known”
  Clients initiate contact to server
Synchronous request/reply protocol
  Runs over TCP, Port 80
Stateless
ASCII format
  Before HTTP/2

## Slide 34: Steps in HTTP request/response
Client
Server
TCP syn
TCP syn + ack
TCP ack + HTTP GET
.
.
.
Establish
TCP connection
Request
response
Client
request
Close connection

## Slide 35: Method types (HTTP 1.1)
GET, HEAD
POST
  Send information (e.g., web forms)
PUT
  Uploads file in entity body to path specified in URL field
DELETE
  Deletes file specified in the URL field

## Slide 36: Client-to-server communication
GET /somedir/page.html HTTP/1.1
Host: www.someschool.edu
User-agent: Mozilla/4.0
Connection: close
Accept-language: fr
(blank line)
HTTP Request Message
  Request line: method, resource, and protocol version
request line
header
lines
carriage return line feed
indicates end of message

## Slide 37: Client-to-server communication
GET /somedir/page.html HTTP/1.1
Host: www.someschool.edu
User-agent: Mozilla/4.0
Connection: close
Accept-language: fr
(blank line)
HTTP Request Message
  Request line: method, resource, and protocol version
  Request headers: provide info or modify request
  Body: optional data (e.g., to “POST” data to server)
request line
header
lines
carriage return line feed
indicates end of message

## Slide 38: Server-to-client communication
HTTP Response Message
  Status line: protocol version, status code, status phrase
  Response headers: provide information
  Body: optional data
HTTP/1.1 200 OK
Connection close
Date: Thu, 06 Jan 2017 12:00:15 GMT
Server: Apache/1.3.0 (Unix)
Last-Modified: Mon, 22 Jun 2006 ...
Content-Length: 6821
Content-Type: text/html
(blank line)
data data data data data ...
status line
(protocol, status code, status phrase)
header lines
data
e.g., requested HTML file

## Slide 39: HTTP is stateless
Each request-response treated independently
  Servers not required to retain state
Good: Improves scalability on the server-side
  Failure handling is easier
  Can handle higher rate of requests
  Order of requests doesn’t matter
Bad: Some applications need persistent state
  Need to uniquely identify user or store temporary info
  e.g., Shopping cart, user profiles, usage tracking, …
Notes: Fate sharing

## Slide 40: How does a stateless protocol keep state?

## Slide 41: State in a stateless protocol: Cookies
Client-side state maintenance
  Client stores small state on behalf of server
  Client sends state in future requests to the server
Can provide authentication
Request
Response
Set-Cookie: XYZ
Request
Cookie: XYZ
DB
Store Cookie
Client
Server
DB
Notes: Creates a notion of a “SESSION” for the user
Customize the user experience
Statefulness comes from the client side

## Slide 42: Beyond cookies
Cookies provide excellent marketing opportunities and create concerns for privacy
  Advertising companies tracks your preferences and viewing history across sites
Many are trying to replace personalized cookies with group-based identifiers
  Example: FLoC in Google Chrome that uses federated learning

## Slide 43: Improve HTTP performance

## Slide 44: Performance goals
User
  Fast downloads (not identical to low-latency communication!)
  High availability
Content provider
  Happy users (hence, above)
  Cost-effective infrastructure
Network (secondary)
  Avoid overload

## Slide 45: Solutions?
User
  Fast downloads (not identical to low-latency communication!)
  High availability
Content provider
  Happy users (hence, above)
  Cost-effective infrastructure
Network (secondary)
  Avoid overload
Improve networking protocols including HTTP, TCP, etc.

## Slide 46: Solutions?
User
  Fast downloads (not identical to low-latency communication!)
  High availability
Content provider
  Happy users (hence, above)
  Cost-effective infrastructure
Network (secondary)
  Avoid overload
Improve networking protocols including HTTP, TCP, etc.
Caching and replication

## Slide 47: Solutions?
User
  Fast downloads (not identical to low-latency communication!)
  High availability
Content provider
  Happy users (hence, above)
  Cost-effective infrastructure
Network (secondary)
  Avoid overload
Improve networking protocols including HTTP, TCP, etc.
Caching and replication
Exploit economies of scale; e.g., webhosting, CDNs, datacenters

## Slide 48: HTTP performance
Most Web pages have multiple objects
  e.g., HTML file and a bunch of embedded images
How do you retrieve those objects (naively)?
  One item at a time
New TCP connection per (small) object!

## Slide 49: Object request response time
RTT (round-trip time)
  Time for a small packet to travel from client to server and back
Response time
  1 RTT for TCP setup
  1 RTT for HTTP request and first few bytes
  Transmission time
  Total = 2RTT + Transmission Time
Client
Server
TCP syn
TCP syn + ack
TCP ack + HTTP GET
RTT
RTT
Tx

## Slide 50: Non-persistent connections
Default in HTTP/1.0
2RTT+△ for each object in the HTML file!
  One more 2RTT+△ for the HTML file itself
Doing the same thing over and over again
  Inefficient

## Slide 51: Concurrent requests and responses
Use multiple connections in parallel
Does not necessarily maintain order of responses
Client = 
Content provider = 
Network =  Why?
R1
R2
R3
T1
T2
T3
Client
Server

## Slide 52: Persistent connections
Maintain TCP connection across multiple requests
  Including transfers subsequent to current page
  Client or server can tear down connection
Advantages
  Avoid overhead of connection set-up and tear-down
  Allow underlying layers (e.g., TCP) to learn about RTT and bandwidth characteristics
Default in HTTP/1.1

## Slide 53: Pipelined requests & responses
Batch requests and responses to reduce the number of packets
  Multiple requests can be contained in one TCP segment
Data are sent in a FIFO manner
  Can lead to head-of-line (HOL) blocking if many small responses follow a large one
  Not supported by default by major browsers circa 2015
Solution
  Priority and preemption
Client
Server
Request 1
Request 2
Request 3
Transfer 1
Transfer 2
Transfer 3
Notes: HTTP/1.1 allows multiple HTTP requests to be written out to a socket together without waiting for the corresponding responses. The requestor then waits for the responses to arrive in the order in which they were requested. The act of pipelining the requests can result in a dramatic improvement in page loading times, especially over high latency connections.

## Slide 54: Scorecard: Getting n small objects
Time dominated by latency
One-at-a-time: ~2n RTT
m concurrent: ~2[n/m] RTT
Persistent: ~ (n+1) RTT
Pipelined: ~2 RTT
Pipelined and Persistent: ~2 RTT first time; RTT later for another n from the same site

## Slide 55: Scorecard: Getting n large objects each of size F
Time dominated by TCP throughput BC (<= BL), where link bandwidth is referred by BL
One-at-a-time: ~ nF/BC
m concurrent: ~ nF/(mBC)
  Assuming each TCP connection gets the same throughput and mBC <= BL
Pipelined and/or persistent: ~ nF/BC
  The only thing that helps is higher throughput

## Slide 56: Summary
Socket programming
HTTP/1.1
  Text-based protocol
  Replaced by binary HTTP/2 protocol, which is being replaced by HTTP/3
Many ways to improve performance
  Pipelining and batching
  Caching in proxies and CDNs （next lecture）
  Datacenters