## Slide 1: CSCI4430 Computer Networks Course Review
Hong Xu, Henry
CSE@CUHK, 2023
Material with thanks to Patrick Lee, Mosharaf Chowdhury, Aditya Akella, Sugih Jamin, Philip Levis, Sylvia Ratnasamy, Peter Steenkiste, and many other colleagues.

## Slide 2: Logistics
Closed-book, but can use one A4 aid-sheet
  Two-sided
Answer all five questions, each focusing on a particular lecture topic
Format similar to last year

## Slide 3: General guidelines (1)
Only assumes material covered in lecture, tutorials, and quizzes
The test doesn’t require you to do complicated calculations
  Use this as a hint to determine if you’re on right track
You don’t need to memorize anything
You do need to understand how things work

## Slide 4: General guidelines (2)
Be prepared to:
  Weigh design options outside of the context we studied them in
  Contemplate new designs we haven’t covered in detail but can be put together
    e.g., I introduce a new IP address format; how does this affect…
  Reason from what you know about the pros/cons of solutions we did study

## Slide 5: This review
Walk through what you’re expected to know at this point: key topics, important aspects of each
Not covered in review does NOT imply you don’t need to know it
  But if it’s covered today, you should know it
Flip through them
  Let me know on Piazza if you need more explanation

## Slide 6: Topics
Basics (lectures 1–2)
Application layer (lectures 3–5)
  HTTP, DNS, CDN, Video Streaming
Transport layer (lectures 6–9)
  UDP vs. TCP
  TCP details: reliability and flow control
  TCP congestion control

## Slide 7: Topics
Network layer (lectures 10–15)
  Overview
  Routers
  Intra-domain routing
  Inter-domain routing
  SDN
Link layer (lecture 16)
  Ethernet

## Slide 8: Basic concepts
You should know:
  Packet vs. circuit switching
  Statistical multiplexing
  Link characteristics
  Packet delays

## Slide 9: Switched networks
End-systems and networks connected by switches instead of directly connecting them
Allows us to scale
  For example, directly connecting N nodes to each other would require N2 links!

## Slide 10: Two approaches to sharing
Packet switching
  Network resources consumed on demand per-packet
  Admission control: per packet
Circuit switching
  Network resources reserved a priori at “connection” initiation
  Admission control: per connection

## Slide 11: Statistical multiplexing
Allowing more demands than the network can handle
  Hoping that not all demands are required at the same time
  Good for bursty traffic (average << peak demand)
  Packet switching exploits statistical multiplexing better than circuit switching

## Slide 12: Delay
Consists of four components
  Transmission delay
  Propagation delay
  Queuing delay
  Processing delay
due to link properties
due to traffic mix and
switch internals

## Slide 13: End-to-end delay
transmission
propagation
queueing
processing
transmission
propagation
queueing
processing
transmission
propagation

## Slide 14: Layers
Layer: a part of a system with well-defined interfaces to other parts
One layer interacts only with layer above and layer below
Two layers interact only through the interface between them

## Slide 15: Layers in practice
Lower three layers implemented everywhere
Top two layers implemented only at hosts
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch
Notes: Why go up? Why not stay down in the lower levels?

## Slide 16: Layer encapsulation: Protocol headers
TCP header
IP header
Ethernet
header
HTTP
request/response
User A
User B
Notes: Deepest level most header

## Slide 17: IP is the narrow waist of the layering hourglass
SMTP
HTTP
TCP
UDP
IP
PPP
FDDI
Ethernet
PSTN
Radio
Copper
Optical
NTP
DNS

## Slide 18: Topics
Basics (lectures 1–2)
Application layer (lectures 3–5)
  HTTP, DNS, CDN, Video Streaming

## Slide 19: Hyper Text Transfer Protocol (HTTP)
Client-server architecture
  Server is “always on” and “well known”
  Clients initiate contact to server
Synchronous request/reply protocol
  Runs over TCP, Port 80
Stateless
ASCII format
  Before HTTP/2

## Slide 20: Object request response time
RTT (round-trip time)
  Time for a small packet to travel from client to server and back
Response time
  1 RTT for TCP setup
  1 RTT for HTTP request and first few bytes
  Transmission time
  Total = 2RTT + Transmission Time
Client
Server
TCP syn
TCP syn + ack
TCP ack + HTTP GET
RTT
RTT
Tx

## Slide 21: Improving HTTP performance
Optimizing connections using three “P”s
  Persistent connections
  Parallel/concurrent connections
  Pipelined transfers over the same connection
Caching
  Forward proxy: close to clients
  Reverse proxy: close to servers
Replication

## Slide 22: Scorecard: Getting n small objects
Time dominated by latency
One-at-a-time: ~2n RTT
m concurrent: ~2[n/m] RTT
Persistent: ~ (n+1) RTT
Pipelined: ~2 RTT
Pipelined and Persistent: ~2 RTT first time; RTT later for another n from the same site

## Slide 23: Scorecard: Getting n large objects each of size F
Time dominated by TCP throughput BC (<= BL), where link bandwidth is referred by BL
One-at-a-time: ~ nF/BC
m concurrent: ~ nF/(mBC)
  Assuming each TCP connection gets the same throughput and mBC <= BL
Pipelined and/or persistent: ~ nF/BC
  The only thing that helps is higher throughput

## Slide 24: Content Distribution Networks (CDN)
Caching and replication as a service
Combination of caching and replication
  Pull: Direct result of clients’requests (caching)
  Push: Expectation of high access rate (replication)

## Slide 25: Hierarchies in the DNS
Three intertwined hierarchies
  Hierarchical namespace
    As opposed to flat namespace
  Hierarchically administered
    As opposed to centralized
  (Distributed) hierarchy of servers
    As opposed to centralized storage

## Slide 26: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers

## Slide 27: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 28: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 29: Name resolution
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 30: Name resolution: Recursive
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?
(mydns.umich.edu)

## Slide 31: Name resolution: Iterative
DNS client (me.cse.umich.edu)
DNS server
root servers
local
.edu servers
nyu.edu servers
www.nyu.edu?

## Slide 32: DNS caching
Performing all these queries takes time
  Up to 1-second latency before starting download
Caching can greatly reduce overhead
  The top-level servers very rarely change
  Popular sites (e.g., www.google.com) visited often
  Local DNS server often has the information cached
How DNS caching works
  DNS servers cache responses to queries
  Responses include a “time to live” (TTL) field
  Server deletes cached entry after TTL expires

## Slide 33: HTTP streaming
Video is stored at an HTTP server with a URL
Clients send a GET request for the URL
Server sends the video file as a stream
Client first buffers for a while to minimize interruptions later
Once the buffer reaches a threshold
  The video plays in the foreground
  More frames are downloaded in the background

## Slide 34: DASH : Dynamic Adaptive Streaming over HTTP
Keep multiple resolutions of the same video
  Stored in a manifest file in the HTTP server
Client asks for the manifest file first to learn about the options
Asks for chunks at a time and measures available bandwidth while they are downloaded
  Low bandwidth ⇒ switch to lower bitrate
  High bandwidth ⇒ switch to higher bitrate

## Slide 35: Applications
Common theme: parallelism
  Applications decomposed into tasks
  Running in parallel on different machines
Two common paradigms
  Partition-Aggregate
  Map-Reduce

## Slide 36: Traditional datacenter networks
Rack
Aggregation
Core

## Slide 37: Challenges
Not enough bandwidth
  Oversubscription: Less bandwidth in the ToR-Agg links than all the servers’ bandwidth in the rack
  Oversubscription ratio: Ratio between bandwidth underneath and bandwidth above
Not enough paths between server pairs
  Load balancing issues
  Failure recovery issues

## Slide 38: Modern datacenter networks: More bandwidth, more paths
Rack
Aggregation
Core

## Slide 39: Clos topology
Multi-stage network
k pods, where each pod has two layers of k/2 switches
  k/2 ports up and k/2 down
All links have the same b/w
At most k3/4 machines
Example
  k = 4
  16 machines
For k=48, 27648 machines
Pod 1
Pod 2
Pod 3
Pod 4

## Slide 40: Topics
Basics (lectures 1–2)
Application layer (lectures 3–5)
Transport layer (lectures 6–9)

## Slide 41: Role of the transport layer
(1) Communication between application processes
  Mux and demux from/to application processes
  Implemented using ports
(2) Provide common end-to-end services for app layer
  Reliable, in-order data delivery
  Well-paced data delivery

## Slide 42: UDP vs. TCP
 | UDP | TCP
Data abstraction | Packets (datagrams) | Stream of bytes of arbitrary length
Service | Best-effort (same as IP) | Reliability In-order delivery Congestion control Flow control
  Both UDP and TCP perform mux/demux via ports

## Slide 43: Reliable transport: General concepts
Checksums (for error detection)
Timers (for loss detection)
Acknowledgments (feedback from receiver)
  Cumulative: “received everything up to X”
  Selective: “received X”
Sequence no (detect duplicates, accounting)
Sliding windows (for efficiency)
You should know:
what these concepts are
why they exist
how TCP uses them

## Slide 44: Designing a reliable transport protocol
Stop and wait is correct but inefficient
  Works packet by packet (of size DATA)
  Throughput is (DATA/ RTT)
Sliding window: use pipelining to increase throughput
  n packets at a time results in higher throughput
  MIN(n*DATA/RTT, Link Bandwidth)

## Slide 45: The TCP abstraction
TCP delivers a reliable, in-order, byte stream
Reliable: TCP resends lost packets (recursively)
  Until it gives up and shuts down connection
In-order: TCP only hands consecutive chunks of data to application
Byte stream: TCP assumes there is an incoming stream of data, and attempts to deliver it to app

## Slide 46: Things to know about TCP
How TCP achieves reliability
RTT estimation
Connection establishment/teardown
Flow Control
Congestion Control
For each, know how the functionality is implemented and why it is needed

## Slide 47: Reliability
Having TCP take care of it simplifies application development
How
  Checksums and timers (for error and loss detection)
  Fast retransmit (to detect faster-than-timeout loss)
  Cumulative ACKs (receiver feedback: what’s lost?)
  Sliding windows (for efficiency)
  Buffers at sender (hold packets until ACKs arrive)
  Buffers at receiver (to reorder packets before delivery to application)

## Slide 48: Establishing/terminating a TCP connection
Three-way handshake to establish connection
  Host A sends a SYN (open; “synchronize sequence numbers”) to host B
  Host B returns a SYN acknowledgment (SYN ACK)
  Host A sends an ACK to acknowledge the SYN ACK
Three-way handshake to terminate (normal operation)
SYN
SYN ACK
ACK
A
B
Data
Data

## Slide 49: Flow control
Why?
  TCP at the receiver must buffer a packet until all packets before it (in byte-order) have arrived and the receiving application has consumed available bytes
  Hence, receiver advances its window when the receiving application consumes data
  Sender advances its window when new data ACK’d
  Risk of sender overrunning the receiver’s buffers
How?
  “Advertised Window” field in TCP header

## Slide 50: Congestion control
Why?
  Because the network itself can be the bottleneck
  Should make efficient use of available network capacity
    While sharing available capacity fairly with other flows
    And adapting to changes in available capacity
How?
  Dynamically adapts the size of the sending window

## Slide 51: Put together
Flow Control
  Restrict window to RWND to make sure that the receiver isn’t overwhelmed
Congestion Control
  Restrict window to CWND to make sure that the network isn’t overwhelmed
Together
  Restrict window to min{RWND, CWND} to make sure that neither the receiver nor the network are overwhelmed

## Slide 52: CC implementation
States at sender
  CWND (initialized to a small constant)
  ssthresh (initialized to a large constant)
  dupACKcount and timer
Events
  ACK (new data)
  dupACK (duplicate ACK for old data)
  Timeout

## Slide 53: Event: ACK (new data)
If CWND < ssthresh
  CWND += 1
CWND packets per RTT
Hence, after one RTT with no drops: CWND = 2xCWND

## Slide 54: Event: ACK (new data)
If CWND < ssthresh
  CWND += 1
Else
  CWND = CWND + 1/CWND
Slow start phase
CWND packets per RTT
Hence, after one RTT with no drops: CWND = CWND + 1
Congestion avoidance phase

## Slide 55: Event: TimeOut
On Timeout
  ssthresh  CWND/2
  CWND  1

## Slide 56: Event: dupACK
dupACKcount ++
If dupACKcount = 3 /* fast retransmit */
  ssthresh = CWND/2
  CWND = CWND/2

## Slide 57: Example
t
Window
Slow-start restart: Go back to CWND = 1 MSS, but take advantage of knowing the previous value of CWND
Slow start in operation until it reaches half of previous CWND, i.e., SSTHRESH
Timeout
Fast Retransmission
SSThresh
Set to Here

## Slide 58: TCP flavors
TCP-Tahoe
  CWND =1 on 3 dupACKs
TCP-Reno
  CWND =1 on timeout
  CWND = CWND/2 on 3 dupACKs
TCP-newReno
  TCP-Reno + improved fast recovery
TCP-SACK
  Incorporates selective acknowledgements

## Slide 59: A simple model for TCP throughput
A
Loss
time
cwnd
1
RTT
½ Wmax RTTs between drops
Avg. ¾ Wmax packets per RTTs

## Slide 60: A simple model for TCP throughput
in MSS
A
Loss
time
cwnd
½ Wmax RTTs between drops
Avg. ¾ Wmax packets per RTTs

## Slide 61: Topics
Basics (lectures 1–2)
Application layer (lectures 3–5)
Transport layer (lectures 6–9)
Network layer (lecture 10–15)

## Slide 62: Network layer
Present everywhere
Performs addressing, forwarding, and routing, among other tasks
Transport
Network
Datalink
Physical
Transport
Network
Datalink
Physical
Network
Datalink
Physical
Application
Application
End system
End system
Switch

## Slide 63: Forwarding vs. routing
Forwarding: “data plane”
  Directing one data packet
  Each router using local routing state
Routing: “control plane”
  Computing the forwarding tables that guide packets
  Jointly computed by routers using a distributed algorithm

## Slide 64: Forwarding
umich.edu
mit.edu
111010010
MIT
#1
#2
#3
#4
Destination | Next Hop
UMICH | 1
UCB | 3
MIT | 2
NYU | 4
Forwarding Table

## Slide 65: Designing the IP header
Think of the IP header as an interface
  Between the source and destination end-systems
  Between the source and network (routers)
Designing an interface
  What task(s) are we trying to accomplish?
  What information is needed to do it?
Header reflects information needed for basic tasks

## Slide 66: What information do we need?
Parse packet
  IP version number (4 bits), packet length (16 bits)
Carry packet to the destination
  Destination’s IP address (32 bits)
Deal with problems along the way
  Loops: TTL (8 bits)
  Corruption: checksum (16 bits)
  Packet too large: fragmentation fields (32 bits)

## Slide 67: IPv4 and IPv6 header comparison
Version | IHL | Type of Service | Total Length |  | 
Identification |  |  | Flags | Fragment Offset | 
Time to Live |  | Protocol | Header Checksum |  | 
Source Address |  |  |  |  | 
Destination Address |  |  |  |  | 
Options |  |  |  |  | Padding
Version | Traffic Class | Flow Label |  | 
Payload Length |  |  | Next Header | Hop Limit
128-bit Source Address |  |  |  | 
128-bit Destination Address |  |  |  | 
IPv4
IPv6
Field name kept from IPv4 to IPv6
Fields not kept in IPv6
Name & position changed in IPv6
New field in IPv6

## Slide 68: Philosophy of changes
Don’t deal with problems: leave to ends
  Eliminated fragmentation and checksum
  Why retain TTL?
Simplify handling:
  New options mechanism (uses next header)
  Eliminated header length
    Why couldn’t IPv4 do this?
Provide general flow label for packet
  Not tied to semantics
  Provides great flexibility

## Slide 69: Input linecards
Main challenge is processing speeds
Tasks involved:
  Update packet header (easy)
  LPM lookup on destination address (harder)
Mostly implemented with specialized hardware

## Slide 70: Looking up the output port
One entry for each address  4 billion entries!
For scalability, addresses are aggregated
Notes: How does a router determine which output port for the packet!

## Slide 71: Longest prefix matching
110000**
110001**
1100****
1101****
ISP Router
Port 1
Port 2
Port 3
Port 4
Send to the port with the longest prefix match

## Slide 72: Tree structure
00*
000
001
0
1
01*
010
011
0
1
11*
110
111
0
1
10*
100
101
0
1
0**
0
1
1**
0
1
***
0
1
000  Port 1
001  Port 2
0**  Port 3
1**  Port 4
Record port associated with latest match, and only override when it matches another prefix during walk down tree
Notes: Idea: build tree to help with match. When a new packet comes in, walk the tree to determine the correct port.
Each level in the tree: one bit. Root: all wild cards

## Slide 73: Output linecards
Packet classification: map packets to flows
Buffer management: decide when and which packet to drop
Scheduler: decide when and which packet to transmit
Scheduler
flow 1
flow 2
flow n
Classifier
Buffer management

## Slide 74: Max-Min fairness
Given set of bandwidth demands ri and total bandwidth C, max-min bandwidth allocations are:
  ai = min(f, ri)
  where f is the unique value such that Sum(ai) = C
r1
r2
r3
?
?
?
C bits/s
Notes: If you don’t get full demand, no one gets more than you.

## Slide 75: Example
C = 10; r1 = 8, r2 = 6, r3 = 2; N = 3
C/3 = 3.33 
  r3 needs only 2
    Can service all of r3
  Remove r3 from the accounting: C = C – r3 = 8; N = 2
C/2 = 4 
  Can’t service all of r1 or r2
  So hold them to the remaining fair share: f = 4
8
6
2
4
4
2
f = 4:
min(8, 4) = 4
min(6, 4) = 4
min(2, 4) = 2
10

## Slide 76: Max-Min fairness
Given set of bandwidth demands ri and total bandwidth C, max-min bandwidth allocations are:
  ai = min(f, ri)
  where f is the unique value such that Sum(ai) = C
If you don’t get full demand, no one gets more than you
This is what round-robin service gives if all packets are the same size

## Slide 77: Routing: Local vs. global view
Local routing state is the forwarding table in a single router
  By itself, the state in a single router cannot be evaluated
  It must be evaluated in terms of the global context
Global state refers to the collection of forwarding tables in each of the routers
  Global state determines which paths packets take

## Slide 78: “Valid” routing state
Global state is “valid” if it produces forwarding decisions that always deliver packets to their destinations
Goal of routing protocols: compute valid state
  How can we tell if routing state if valid?
Notes: What could go wrong?

## Slide 79: Necessary and sufficient condition
Global routing state is valid if and only if:
  There are no dead ends (other than destination)
  There are no loops
A dead end is when there is no outgoing link (next-hop)
  A packet arrives, but the forwarding decision does not yield any outgoing link
A loop is when a packet cycles around the same set of nodes forever

## Slide 80: Least-cost routes
Least-cost routes provide an easy way to avoid loops
  No reasonable cost metric is minimized by traversing a loop
Least-cost paths form a spanning tree for each destination rooted at that destination

## Slide 81: Intra-domain routing
Link-state (LS) routing protocol
  Dijkstra’s algorithm
  Broadcast neighbors’ info to everyone
Distance vector (DV) routing protocol
  Bellman-Ford algorithm
  Gossip to neighbors about everyone

## Slide 82: Similarities between LS and DV routing
Both are shortest-path based routing
  Minimizing cost metric (link weights) a common optimization goal
    Routers share a common view as to what makes a path “good” and how to measure the “goodness” of a path
Due to shared goal, commonly used inside an organization
  RIP and OSPF are mostly used for intra-domain routing

## Slide 83: Comparison of LS and DV routing
Messaging complexity
LS: with N nodes, E links, O(NE) messages sent
DV: exchange between neighbors only
Speed of convergence
LS: relatively fast
DV: convergence time varies
  Count-to-infinity problem
Robustness: what happens if router malfunctions?
LS:
  Node can advertise incorrect link cost
  Each node computes its own table
DV:
  Node can advertise incorrect path cost
  Each node’s table used by others (errors propagate)

## Slide 84: Addressing is key to scalable inter-domain routing
Ability to aggregate addresses is crucial for
  State: Small forwarding tables at routers
    Much less than the number of hosts
  Churn: Limited rate of change in routing tables

## Slide 85: Classful addressing
Three classes
  8-bit network prefix (Class A),
  16-bit network prefix (Class B), or
  24-bit network prefix (Class C)
Example: an organization needs 500 addresses.
  A single class C address is not enough (<500 hosts)
  Instead, a class B address is allocated (~65K hosts)
    Huge waste!

## Slide 86: CIDR: Classless inter-domain routing
Flexible division between network and host addresses
Offers a better tradeoff between size of the routing table and efficient use of the IP address space

## Slide 87: Hierarchy in IP addressing
32 bits are partitioned into a prefix and suffix components
Prefix is the network component; suffix is the host component
Inter-domain routing operates on network prefix
00001100
00100010
10011110
00000101
Network (23 bits)
Host (9 bits)
12
34
158
5

## Slide 88: Administrative structure shapes Inter-domain routing
ASes want freedom to pick routes based on policy
ASes want autonomy
ASes want privacy

## Slide 89: Business relationships
peer
peer
provider
customer
Relations between ASes
Customers pay provider
Peers don’t pay each other
Business implications

## Slide 90: Routing follows the money!
A
B
C
D
E
F
Q
Pr
Cu
Peer
Peer
traffic allowed
traffic not allowed
ASes provide “transit” between their customers
Peers do not provide transit between other peers

## Slide 91: BGP inspired by Distance-Vector with four differences
Shortest-path routes may not be picked to enforce policy
Path-Vector routing to avoid loops
Selective route advertisement may affect reachability
Routes may be aggregated for scalability

## Slide 92: BGP: Basic idea
Each AS selects the “best” route it hears advertised for a prefix
An AS advertises (“exports”) its best routes to one or more IP prefixes
Notes: Arrows are routing message

## Slide 93: Policy dictates how routes are “selected” and “exported”
Selection: Which path to use?
  Controls whether/how traffic leaves the network
Export: Which path to advertise?
  Controls whether/how traffic enters the network
Can reach 128.3/16
blah blah
Route selection
A
P
C
B
Q
Route export
Notes: Arrows: routing messages!

## Slide 94: Typical export policy
Destination prefix advertised by… | Export route to…
Customer | Everyone (providers, peers, other customers)
Peer | Customers
Provider | Customers
We’ll refer to these as the “Gao-Rexford” rules
(capture common – but not required! – practice)

## Slide 95: Selection using attributes
Rules for route selection in priority order
Priority | Rule | Remarks
1 | LOCAL PREF | Pick highest LOCAL PREF
2 | ASPATH | Pick shortest ASPATH length
3 | MED | Lowest MED preferred
4 | eBGP > iBGP | Did AS learn route via eBGP (preferred) or iBGP?
5 | iBGP path | Lowest IGP cost to next hop (egress router)
6 | Router ID | Smallest next-hop router’s IP address as tie-breaker

## Slide 96: Topics
Network layer (lectures 10–15)
  Intra-domain routing
  Inter-domain routing
  SDN
Link layer (lectures 16–17)
  Ethernet

## Slide 97: Data link layer
Provides four primary services
  Framing
    Encapsulates network layer data
  Link access
    Medium access control (MAC) protocol defines when to transmit frames
  Reliable delivery
    Primarily for mediums with high error rates (e.g., wireless)
  Error detection and correction

## Slide 98: Random access MAC protocols
When node has packet to send
  Transmit at full channel data rate w/o coordination
Two or more transmitting nodes  collision
  Data lost
Random access MAC protocol specifies
  How to detect and recover from collisions
Examples
  ALOHA and Slotted ALOHA
  CSMA, CSMA/CD, CSMA/CA (wireless)

## Slide 99: CSMA (Carrier Sense Multiple Access)
CSMA: listen before transmit
  If channel sensed idle: transmit entire frame
  If channel sensed busy, defer transmission
Human analogy: don’t interrupt others!
Does not eliminate all collisions
  Why?

## Slide 100: CSMA/CD (Collision Detection)
CSMA/CD: carrier sensing, deferral as in CSMA
  Collisions detected within short time
  Colliding transmissions aborted, reducing wastage
Collision detection easy in wired (broadcast) LANs
  Compare transmitted, received signals
Collision detection difficult in wireless LANs
Notes: wireless: because reception while tx is difficult . broadcast isn’t perfect so collisions local

## Slide 101: Why switched Ethernet?
Enables concurrent communication
  Host A can talk to C, while B talks to D
  No collisions and no need for CSMA/CD
  No constraints on link lengths, etc.
Ethernet switch
A
B
C
D

## Slide 102: Ethernet switches are “self learning”
When a packet arrives:
  Inspect source MAC address, associate with incoming port
  Store mapping in the switch table
  Use time-to-live field to eventually forget mapping
A
B
C
D
Packet tells switch how to reach A.

## Slide 103: ARP and DHCP
Link layer discovery protocols
  ARP  Address Resolution Protocol
  DHCP  Dynamic Host Configuration Protocol
  Confined to a single local-area network (LAN)
  Rely on broadcast capability

## Slide 104: Key ideas in both ARP and DHCP
Broadcasting: Can use broadcast to make contact
  Scalable because of limited size
Caching: remember the past for a while
  Store the information you learn to reduce overhead
Soft state: eventually forget the past
  Associate a time-to-live field with the information
  … and either refresh or discard the information
  Key for robustness in the face of unpredictable change

## Slide 105: ARP: Address Resolution Protocol
Every host maintains an ARP table
  List of (IP address  MAC address) pairs
Consult the table when sending a packet
  Map dest. IP address to dest. MAC address
  Encapsulate (IP) data packet with MAC header; xmit
What if IP address not in the table?
  Sender broadcasts: Who has IP address 1.2.3.156?
  Receiver replies: MAC address 58-23-D7-FA-20-B0
  Sender caches result in its ARP table

## Slide 106: What if the destination is remote?
Look up the MAC address of the first hop router
  1.2.3.48 uses ARP to find MAC address for first-hop router 1.2.3.19 rather than ultimate destination IP address
How does the red host know the destination is not local?
  Uses netmask (discovered via DHCP)
How does the red host know about 1.2.3.19?
  Also DHCP
host
host
DNS
...
host
host
host
...
router
router
1.2.3.0/24 (255.255.255.0)
5.6.7.0/24
1.2.3.156
1.2.3.48
1.2.3.19
router

## Slide 107: This is it!
THANK YOU SO MUCH!!!